## Slide 1: SDN Security Introduction
Chris Shenefiel

## Slide 2: What we will cover…
What is SDN
Security considerations
Review of SDN Security: A Survey
Background of LXC, KVM/QEMU and Xen
Questions

## Slide 3: The network paradigm as we now it….
Control and Data Plane resides within Physical Device

## Slide 4: What SDN means
In the SDN paradigm, not all processing happens inside the same device
Notes: Genesis : Stanford University – Clean Slate Project
OpenFlow is a Layer 2 communications protocol that gives access to the forwarding plane of a network switch or router over the network
OpenFlow is a subset of SDN as defined by the Open Networking Foundation

## Slide 5: How SDN is implemented
Multiple applications sending updates to a controller
Controller monitors state of network devices and updates
Updates are synchronized and managed by controller
Controller
Data Plane
Data Plane
Data Plane
Application
Application
Application

## Slide 6: Authorization/Authentication Vulnerability
Controller
Data Plane
Data Plane
Data Plane
Authenticate between applications and controllers
Recommendation TLS mutual authentication between controller and switches
Application
Application
Application

## Slide 7: Side-channel attacks
Peer into flow rules on the input buffer to learn traffic routing
Monitor packet delays through the data plane to infer the amount of processing done for a given packet
Controller
Data Plane
Data Plane
Data Plane
Application
Application
Application

## Slide 8: Denial of Service attacks
Overload the switches by flooding the data communications channel
Overload the switch flow table with too many entries
Controller
Data Plane
Data Plane
Data Plane
Application
Application
Application

## Slide 9: Authentication and Integrity Vulnerability
Controller
Data Plane
Data Plane
Data Plane
Propose inserting a flow verification stage
  Prevents bad configurations from hitting network
  Can model network and test updates for damaging consequences
Limitations:
  Most only support one controller
  Added overhead impacts performance
VeriFlow/FlowChecker/FlowVisor
Application
Application
Application

## Slide 10: Configuration Vulnerability
Controller
Data Plane
Data Plane
Data Plane
Policy enforcement
  Do configuration changes violate our information security or control policies
  Auditing to prove that the network configuration conforms to polices and regulations
Authentication
  Are you really who you say you are
Application
Application
Application

## Slide 11: SDN Security Benefits
Dynamically re-route traffic
  Contain infected networks/systems
  Send traffic to “middle boxes” for further analysis
  Continuously reconfigure network to confuse attackers (Moving Target Defense)
Increase security visibility
  Monitor or tap any traffic on demand
  Detect DDoS
  Intrusion detection
  Data exfiltration

## Slide 12: 3 Questions
Q: What benefit and liability do SDN “middle boxes” provide?
Q: What areas did the authors highlight as needing further study?
Q: What security issue from Table 1 would you focus on and why?

## Slide 13: Thank You – Questions?